## Slide 1
AI-Powered Godown Monitoring System
for Post-Harvest Loss Prevention
Team InnovativeX
Team ID: H26AGR06
TEAM LEAD
Vandana P.R.
TEAM MEMBERS
Chinnam Rushya
T. Divya Sri
COLLEGE
SASTRA Deemed University
1

## Slide 2
Problem Statement
A large share of India's stored paddy and pulses is lost after harvest, not in the field, but inside the godown, because spoilage (mold, pests, moisture damage) is usually discovered only during infrequent manual inspection, by which point the loss is already done.
Objectives
▸ Continuously monitor godown conditions (temperature, humidity, gas) instead of periodic manual checks
▸ Use computer vision to catch visible spoilage signs (mold, pest damage, discoloration) directly from grain images
▸ Fuse sensor + vision signals into a single, explainable real-time risk score per storage zone
▸ Automatically alert stakeholders via WhatsApp before a zone crosses into high-loss territory
Reactive
Manual inspection finds spoilage after it has already spread
Siloed data
Temp/humidity loggers exist, but rarely fused with vision or alerting
Late alerts
No automatic, real-time notification to stakeholders on rising risk
2
InnovativeX | H26AGR06

## Slide 3
System Design
Simulated / Real Sensors
Temp · Humidity · Gas (CO₂ proxy) per zone
Grain Image Upload
Zone photo via dashboard
FastAPI Backend
main.py — single-process API (serves dashboard too)
CV Classifier MobileNetV2 model
Risk Engine
risk.py — rule-based scoring + sensor/vision fusion
Alert Dispatch
Twilio WhatsApp, with in-app fallback log
Web Dashboard
Polls /risk/{zone} every few seconds, shows zone cards
3

## Slide 4
Algorithms
1. Rule-Based Sensor Risk Scoring
▸ Additive weighted thresholds per signal, capped at 100
▸ Humidity >70% (+20) / >75% (+40) — mold risk
▸ Temperature >30°C (+15) / >32°C (+30) — pest/fungal accelerant
▸ Gas / CO₂ proxy >550ppm (+15) / >700ppm (+30) — early respiration signal
2. Computer-Vision Spoilage Classification
▸ 4 classes: healthy / mold / pest_damage / discoloration
▸ Default: HSV pixel-statistics heuristic (dark+yellow-green → mold, very-dark ratio → pest damage, orange-red patches → discoloration)
▸ Upgrade path: MobileNetV2 transfer learning (frozen ImageNet base + Dense head), trained on Colab GPU
▸ Confidence <60% → labeled "uncertain", flagged for manual check instead of guessing
3. Sensor + Vision Fusion, and Alert Cooldown
▸ CV result adds to sensor score: healthy +0, discoloration +15, pest_damage +25, mold +75 (capped at 100)
▸ Score ≥70 fires a WhatsApp alert; a per-zone cooldown (default 30 min) prevents duplicate alert spam
4

## Slide 5
Technology Stack
Backend / API
Python 3.12, FastAPI, Uvicorn (ASGI server)
Computer Vision
Pillow (HSV heuristic classifier); TensorFlow / Keras + MobileNetV2 transfer learning (trained on Google Colab GPU)
Frontend / Dashboard
HTML5, CSS3, vanilla JavaScript — polling-based live zone cards, no framework overhead
Alerting
Twilio WhatsApp API, with automatic in-app fallback log if not configured
Config / Environment
python-dotenv for credential/config management (.env, gitignored)
File Handling
python-multipart for image upload endpoints
Deployment Model
Single-process architecture — FastAPI serves both the REST API and the static dashboard, avoiding separate frontend hosting or CORS setup
5

## Slide 6
Results
▸ Three simulated godown zones with realistic drifting sensor data; one zone ("leaky roof") escalates over time to demonstrate a live risk story, not flat numbers
▸ Real-time risk score updates correctly as thresholds are crossed, with a human-readable reasons log (e.g. "humidity 76.2% > 75% (high mold risk)")
▸ Image upload → classification pipeline works end-to-end using the HSV heuristic classifier; MobileNetV2 training pipeline is ready to drop in trained weights with zero code changes
▸ Automatic WhatsApp alert dispatch verified via Twilio Sandbox once a zone crosses risk score 70, with graceful fallback to an in-app alert log
▸ Low-confidence vision results (<60%) are correctly flagged "uncertain" instead of a forced label — verified responsible-AI behaviour
Demo Video
[ Insert / embed the recorded demo walkthrough here ]
6

## Slide 7
Comparison with Existing Solutions
Capability
Manual Inspection
Basic IoT Loggers
Our System
Monitoring frequency
Periodic, infrequent
Continuous, sensor-only
Continuous, sensor + vision
Spoilage detection method
Human visual check
None (raw data only)
CV classifier + rule engine
Early-warning signal
None — reactive
Temp/humidity only
Gas/CO₂ as leading indicator, before visible spoilage
Confidence handling
Subjective
N/A
Confidence-aware — flags “uncertain” instead of guessing
Alerting
Manual reporting
Dashboard only, no push alerts
Automatic WhatsApp alert with cooldown
Domain calibration
Inspector experience varies
Generic thresholds
Calibrated for TN paddy/pulses storage
Hardware dependency
None, but slow
Requires hardware upfront
Software-first; hardware swap is a 1-function change
7
InnovativeX | H26AGR06

## Slide 8
Summary & Future Work
Summary
▸ Built and verified an end-to-end AI-powered godown monitoring system: simulated sensors + computer vision + rule-based risk fusion + automated WhatsApp alerting
▸ Fully demoable with zero physical hardware — a software-first MVP that validates the logic and workflow before any hardware investment
▸ Risk thresholds are domain-validated for paddy/pulses storage, not generic assumptions
▸ Architecture is deliberately hardware-agnostic: swapping in real DHT22/MQ sensors is a one-function change
Future Work
▸ Train the MobileNetV2 classifier on real (not synthetic-proxy) grain spoilage images for production-grade accuracy
▸ Integrate physical DHT22 temperature/humidity and MQ-series gas sensors on-site
▸ Split risk thresholds per crop type (paddy vs. pulses have different safe-moisture profiles)
▸ Multi-warehouse dashboard for cooperative or FCI-scale deployment, with historical trend analytics
▸ Move from reactive alerting to predictive risk forecasting
8